Hydrology Lab #1:  Unit Conversions and Precipitation

(Total score: 10 marks, i.e., 10% of final score)

Questions:

1. Unit conversions (1 mark)

1) Length: 	1 m + 2 cm = ? m

2) Speed:  	(100 km + 100 m)/(1 h + 30 minutes) = ? km/h

3) Area:	1 km2 = ? m2

4) Volume: 	1 km3 = ? m3

5) Density:	1 ton/m3=? g/cm3

6) Force:  	1.2 kg ( 9.8 m/s2 = ? Newton

7) Force:   	500 g ( 80 cm/s2 = ? Newton

8) Pressure: 	1 kg ( 9.8 m/s2 ( 2 m 2 = ? Pascal = ? mb

9) Pressure: 	1 ton ( 0.05 km/s2 ( 5 m 2 = ? Pascal = ? mb

10) Energy:	20 J ( 5 s = ? Watts

2. The saturated water vapor pressure in the air is determined solely by the air temperature and can be approximated by the simple equation:

where es is the saturated water vapor pressure in mb, and T is the air temperature in (C. Calculate the es in mb and Pa, respectively, at T=0(C and T=30(C (2 mark)?

3.  According to the equation in question 2, the saturated water vapor pressure is 6.1078 mb at 0 (C. Under the gravity of 9.8 m s-2, what is the total mass (kg) of water vapor that creates this pressure on an area of 1 m2?  (1 mark)

4. In many hydrological studies, rainfall is measured using tipping-bucket rain gauges.  On the separate page is a rainfall chart from a rain gauge for an extreme storm event that occurred at Erindale, Mississauga, Ontario, in October 1995.  Each vertical step (tic mark) on the chart, either moving up or down, represents 2/10 mm, or 0.2 mm of rainfall.  Note that there are two tics per line and the pen mark is offset by one tic to the bottom (in this particular case).

- From the given chart, plot rainfall intensity (mm/h) against time in hourly time steps for October 5 and 6, 1995.  (1 mark)

- Find the maximum amount of rainfall for any 1, 2, 6, 12 and 24 hour durations for the whole 2-day storm event from the 5th to 6th of October 1995 (this is a section of the weekly chart) and complete the following table (2 marks). Note that for a given length of duration (which could be shorter or longer than a rainfall event), there are many rainfall values at different times. Also note that the maximum amount and intensity of rainfall in a given duration are not confined to a calendar day. The maximum amount is the summation of rainfall quantity (in mm) for a given length of time, and the maximum rainfall intensity is the corresponding amount of rainfall per unit time (in mm/h).

Table 1:  Precipitation Data (Erindale, Mississuaga, Ontario)

| Duration (min) | Maximum Amount of Rain (mm) | Maximum Rainfall Intensity (mm/h) |
| --- | --- | --- |
| 60 |  |  |
| 120 |  |  |
| 360 |  |  |
| 720 |  |  |
| 1440 |  |  |

- Plot the maximum amount of rainfall (vertical axis) against duration (horizontal axis) for the event on 4 by 3 cycle log-log paper.  (0.5 mark)

- Plot the maximum rainfall intensity in mm/h (vertical axis) against duration (horizontal axis) for the event on 4 by 3 log-log paper. (0.5 mark)

5. From automatically recorded hourly rainfall data in May-September, 2001, at the Erindale campus, Mississauga, we obtained the following maximum rainfall information for various periods.

Table 2. Maximum rainfall amounts in different durations

| Duration | 1 h | 2 h | 6 h | 12 h | 24 h | 5 d | 10 d | 20 d | 30 d | 60 d | 90 d |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Max. Rainfall (mm) |  |  |  |  |  |  |  |  |  |  |  |

Plot the maximum amount of rainfall (mm) against duration (1, 2, 6, 12, and 24 hours, 5, 10, 20, 30, 60 and 90 days) on a 4 by 3 cycle log-log paper. Compared with Figure 2-15 in Ward and Robinson (2000), what can you find?  (2 marks)

Note: Please hand in your original graphs and charts (not photocopies).  Show sample calculations where appropriate.

# Text boxes

October 7

October 5

October 6